## Slide 1: FIELD PROGRAMMABLE GATE ARRAY
Presented by:
Neha Gour
M.Tech(VLSI Design)

## Slide 2: Contents
Introduction
Evaluation of FPGA
Architecture of FPGA
FPGA classification on user programmable switch technology
FPGA Structural classification
FPGA Design flow
Required tools
Advantages & Disadvantages
Applications

## Slide 4: Introduction
In the world of digital electronics system , there are three basic kind of devices: memory, microprocessor and logic devices.
Memory device to store the random information.
Microprocessor are for execution of instruction to perform a task.
Logic devices provide specific functions.

## Slide 5: (cont..)
An FPGA (Field Programmable Gate Arrays) is a device contains a matrix of reconfigurable gate array logic circuitry for a desired application or function any time after manufacturing by the users.
Combination of general-purpose processors and ASICs (Application-Specific IC).

## Slide 6: Evaluation of FPGA
FPGA
CPLD
PAL
PLA
PROM
Programmable Logic Devices
Fixed Logic Devices
Logic devices

## Slide 7: Difference between CPLD &FPGA
CPLD | FPGA
Coarse grain Architecture | 1. Fine grain Architecture
2. More Faster compare to FPGA | 2. Faster
3. Better for simple applications | 3. Good for complex applications
4. EEPROM based Architecture | 4. RAM based Architecture
5. Cheaper | 5. Expensive
6.Made up of Larger blocks | 6. Made up of Tiny blocks

## Slide 8: Architecture of FPGA
FPGA chip consist of a matrix of CLBs surrounded by a periphery of I/O blocks & signals are routed by the programmable interconnects .

## Slide 9: (cont…)
Configurable Logic Blocks(CLBs)
CLB is a basic component that provides a logic & storage for a target application.
A logic blocks are made up of NAND gate , an interconnection of Multiplexer, LUTs & PAL style wide input gate.
The output of LUT is connected to an optional Flip-Flop. A multiplexer selects the BLE output to be either the output of a Flip-Flop or the LUT.
A CLB can contain a cluster of BLEs connected through a local routing network.

## Slide 10: (cont…)
Modern FPGAs contain typically 4 to 10 BLEs in a single cluster.

## Slide 11: (cont…)
I/O blocks
I/O blocks are storage element ,they are configured by either flip-flops or latches.
Each I/O blocks can be programmed in to :
Input Path
Output Path

## Slide 12: (cont…)
Resources for interconnection
FPGA routing architecture provides connection between Logic blocks & i/o blocks.
Architecture consist of wires & programmable switches that form the connection.
Programmable switches are configured by programmable technology.
There is a trade off between density of Logic blocks & amount of area used up for routing.

## Slide 13: FPGA Classification on user programmable switch technology
FPGA
SRAM Programmed
Antifuse -Programmed
EEPROM Programmed

## Slide 14: FPGA Structural classification
FPGA
Symmetrical arrays
Hierarchical PLDs
Row based architecture

## Slide 15: FPGA Design flow
Design entry
simulation
Synthesis
Place and route
Dump code and Verify

## Slide 16: Required Tools
Text Editor
Xilinx ISE or Vivado
FPGA Development Board

## Slide 17: Advantages & Disadvantages
Advantages of FPGAs
Highest performance.
Ability of Parallel processing.
Provide flexibility of reprogramability to user.
Improvement of Density relative to discrete SSI/MSI component.

## Slide 18: (cont..)
Disadvantages of FPGAs
Delay introduced for product to market, because of increased Design time.
Expensive to Develop.

## Slide 19: Applications
Automotive.
Digital Display.
Medical Electronics.
Telecommunications.
Consumer electronics.
High resolution video.
Digital signal processing etc…