## Slide 1
Reducing Computational complexity of Mathematical functions using FPGA
Neha Gour, M.Tech. (VLSI Design)
Department of Electronics, Banasthali University
Guided by:
Prof. Arup Banerjee
RRCAT, Indore

## Slide 2: Outline
Introduction
Motivation
Conventional Processor vs. FPGA
Basic skeleton of project
Work carried out
Optimization Directives
Addition of Fixed Point Numbers
Addition of Floating Point Numbers
Matrix Multiplication using Integer Numbers
Result and Discussion

## Slide 3: Introduction
Analysis of complex algorithm demand for less execution time and low storage space.
Computationally intensive applications such as machine learning, weather forecasting, big data, computational biology etc.
Require a lot of computation time to execute, because usually the task is sequentially simulated.

## Slide 4: Motivation
To reduce the computation time and make system efficient using concept of parallelism.
Parallel processing through FPGA is one possible solution to reduce execution time.
Objective of this work is to improve the execution time of mathematical functions using optimization directives such as loop pipeline and loop unrolling.

## Slide 5: Conventional Processor vs. FPGA
Conventional Processor | FPGA
Sequential processing device. | Parallel processing device.
Large no. of clock cycles are required to perform a specific task. | Fewer clock cycles are required to execute the task.
It has fixed ALU. | FPGA has programmable ALUs.

## Slide 6: Overview of an FPGA
2-D array of logic blocks with electrically programmable interconnections.
User can configure
Interconnection between logic blocks,
The function of each block.
Figure: Basic structure of FPGA

## Slide 7: Basic Skeleton of the Project
High-Level language (C-program)
LUT 1
LUT 2
LUT 3
Parallel processing through FPGA is implemented using High-Level Synthesis(HLS).

## Slide 8: Work Carried Out
C-Language
APPLYING DIRECTIVES
LOOP PIPELINE
LOOP UNROLL
FPGA
Fig. Basic Block diagram of design
NOTE: HLS is done by Vivado HLS(2017.2) software. Hardware implementation is done using Artix-7 FPGA.

## Slide 9: 1. Sequential loop
A[5]
B[5]
DATA
1
2
3
4
5
1
2
3
4
5
+
+
+
+
+
C[0]
C[1]
C[2]
C[4]
C[3]
For(i=0; i<5; i++)
{
C[i]=A[i]+ B[i];
}

## Slide 10: I. Optimization Directives
1. Loop unrolling
Loop unrolling is a directive that exploits the parallelism between loop iteration.
It creates multiple copies of the loop body and adjust the loop iteration counter accordingly.
Directive command: #pragma HLS UNROLL factor = <INTEGER>.
Unrolled loop
For( i=0;i<5; i++){
C[i]=A[i]+B[i];
C[i+1]=A[i+1]+B[i+1];
.
.
.
C[i+4]=A[i+4]+B[i+4]
}

## Slide 11: cont..
DATA
A[5]
B[5]
1
2
3
4
5
1
2
3
4
5
+
C[0]
+
+
C[1]
C[2]
+
C[3]
+
C[4]

## Slide 12: 2. Loop Pipelining
Loop pipelining allows the operation in a loop to be implemented in a concurrent manner.
In pipelining the next iteration of loop can start before current iteration is finished.
Directive command: #pragma HLS PIPELINE initiation interval(II)* = <INTEGER>.
*Initiation Interval (II) is the number of clock cycles between the start times of consecutive loop iterations.

## Slide 13: cont..
A[5]
B[5]
1
2
3
4
5
1
2
3
4
5
+
+
+
+
+
C[0]
C[1]
C[2]
C[3]
C[4]
DATA

## Slide 14: II. Addition of Fixed-Point Numbers
1. Sequential loop
int i, int A[i], int B[i], int C[i];
For(i=0; i<8; i++) {
C[i]=A[i]+ B[i];
}
Fig. Fixed point addition simulation result of sequential process

## Slide 15: 2. Loop Pipelining
Fig. Fixed point addition simulation result after applying pipelining
For(i=0; i<8; i++)
{
#pragma HLS pipeline II=1;
C[i]=A[i]+ B[i];
}

## Slide 16: 3. Loop Unrolling
Fig. Fixed point addition simulation result after applying unrolling
For(i =0; i<8; i ++) {
C[i]=A[i]+ B[i];
C[i+1]=A[i+1]+ B[i+1];
.
.
.
C[i+7]=A[i+7]+ B[i+7];
}

## Slide 17: Hardware Realization of Fixed-Point Addition 1. Sequential loop
State 1
State 2
State 3
RESET
EXIT CONDITION
OPERATION
EXIT=1
EXIT=0

## Slide 18: 2. Loop pipelining
State 1
State 2
State 3
RESET
EXIT CONDITION
OPERATION
EXIT=0
EXIT=1

## Slide 19: 3. Loop unrolling
State 1
State 2
RESET
EXIT
OPERATION
PARAMETERS | Sequential | Pipeline | Unroll
Loop latency | 17 | 10 | 1
LUTs | 50 | 67 | 117
I/O ports | 142 | 187 | 468
Comparison of computational optimization Directive of fixed-point addition

## Slide 20: III. Addition of Floating Point Numbers
For the addition and multiplication of floating point numbers we have to use floating point IPs.
Numbers written in scientific notation have three components
 | Exponent | Mantissa
Sign
31
30 23
8 bits
22 0
23 bits
1bit
Single precision format(32 bit)

## Slide 21: Floating-point Addition Block diagram(IP)

## Slide 22
1. Sequential loop
int i, float A[i], float B[i], float C[i];
For(i=0; i<8; i++;) {
C[i]=A[i]+ B[i];
}
Fig. Floating point addition simulation result of sequential process

## Slide 23: 2. Loop Pipelining
Fig. Floating point addition simulation result after applying pipelining
3. Loop Unrolling
Fig. Floating point addition simulation result after applying unrolling

## Slide 24: Hardware Realization of Floating-Point Addition
        1. Sequential loop
State 1
State 2
State 8
State 7
State 6
State
5
State 4
State 3
State
9
RESET
EXIT =0
EXIT CONDITION
EXIT =1

## Slide 25: 2. Loop pipelining
OPERATION
RESET
EXIT =0
EXIT =1
25
State 1
State 2
State 3

## Slide 26
3. Loop Unrolling
State 1
State 2
State 3
RESET
State 4

## Slide 27
PARAMETER | Sequential | Pipeline | Unroll
Loop latency | 65 | 14 | 3
LUTs | 272 | 326 | 1771
I/O ports | 104 | 205 | 708
DSP48E | 2 | 2 | 16
Comparison of computational optimization Directive of floating-point addition

## Slide 28: IV. Matrix multiplication using integer numbers
Algorithm of Matrix multiplication
start
Read a[3][3],b[3][3]
For i=0 to 2
For j=0 to 2
For k=0 to 2
rows
C[i][j] += A[i][k] * B[k][j];
columns
product
* Sequential implementation of above code will take 79 clock cycles for completion.
28

## Slide 29
1. Sequential implementation of matrix multiplication
Fig. Matrix multiplication simulation result by conventional method

## Slide 30: Matrix multiplication with integer numbers Block diagram(IP)

## Slide 31: Comparison of computational optimization Directive of Matrix multiplication
PARAMETER | Sequential | Pipelining | Unrolling
Loop latency | 79 | 21 | 10
LUTs | 142 | 282 | 367
I/O ports | 41 | 58 | 270
DSP48E | 1 | 2 | 6

## Slide 32: Results and Conclusion
Applications of optimization directives have explored to reduce execution time.
Loop Pipelining and loop unrolling of fixed-point addition show the reduction in delay by approx. 28% and 71%, and increase in hardware by 14% and 68% respectively, as compared to sequential.
Experimental results demonstrate that, pipelining and unrolling of floating-point addition show the reduction in delay by 72% and 91%, and increase in hardware 2 times and 5 times respectively, as compared to sequential processing. DSP48E increased by 16 from 2 slices compare to the conventional.
Loop Pipelining and loop unrolling of matrix multiplication with integer entries show the reduction in delay by approx. 73% and 87%, and increase in hardware by 30% and nearly 75% respectively, as compared to sequential. In addition increase in DSP48E slices is also observed.
Simulation results show that proposed design has reduced time complexity for mathematical functions.

## Slide 33: References
[1]
[2]
[3]
[4]
[5]

## Slide 34: Acknowledgement
I would like to thank my project coordinator Prof. Arup Banerjee, who gave me the opportunity to do this wonderful project.
I express my sincere thanks and deepest regards to Dr. Srivathsan Vasudevan and Dr. Satya S. Bulusu of IIT Indore who always gave the valuable suggestion and guidance for this work.